## Slide 1: Advances in Multicast - The Promise of Single Source Multicast (SSM) (with a little on multicast DOS)
Marshall Eubanks
Multicast Technologies
tme@on-the-i.com

## Slide 2: What is Multicast ?
The ability to replicate packets inside the network
One stream from the sender can be sent to many recipients
Protocol Independent Multicasting- Sparse Mode is the current standard : Internet Standard Multicast (ISM)

## Slide 3: Why Multicast ?
Because it has a favorable marginal cost for streaming media
Streaming Media over unicast is more expensive to deliver than you can get from advertising
A few months ago, this seemed less important, but now...

## Slide 4: What Are the Holdups ?
If Multicasting is so compelling, why is it not in common use ?
Multicast is very complicated
  Attempt to fit all applications with one transport protocol
  PIM-SM is intended for both one to many and many to many applications
  MSDP, the current solution for inter-domain multicasts, does not scale well.

## Slide 5: Internet Standard Multicast (ISM)
The new name for general multicasting
  Protocol Independent Multicast - Sparse Mode (PIM-SM) plus
  Multicast Source Discovery Protocol - MSDP &
  MultiProtocol BGP (MBGP)
The trouble with ISM is
  Anyone can join a Group
  MSDP doesn’t scale
  PIM-SM requires a Rendezvous Point (RP)
    These are subject to attack

## Slide 6: The Trouble with RP’s
PIM-SM requires at least one RP.
Source (S) sends multicast data to the RP
To join a group, issue a (*,G) join to the RP
The RP sends data down the shared tree.
Later (maybe) a (S,G) join is issued to switch traffic from the shared tree to a shortest path tree.
In general, no mechanism to stop a rogue source from sending data to the RP

## Slide 7: The Trouble with MSDP <draft-ietf-msdp-spec-06.txt>
For each source, a Source Active (SA) message
Certain routers are set up as MSDP peers
These send unicast TCP messages with SA messages
These are peer-flooded through-out the entire multicast enabled Internet
Doesn’t scale well - all peers get all source announcements

## Slide 8: Interdomain ISM is complicated.

## Slide 9: ISM Join - cont’d

## Slide 10: The New SSM Protocol <draft-ietf-pim-sm-v2-new-01.txt> <draft-holbrook-ssm-arch-00.txt>
Single Source Multicast (SSM) is a sub-set of PIM-SM for one to many only
  232 / 8 is assigned to SSM
Edge routers Need IGMP version 3
Interior Routers need list filters to prevent RP (*,G) joins

## Slide 11: SSM is much simpler

## Slide 12: SSM Advantages
No RP
  No need for MSDP
All joins are (S,G), so no need for Class D address allocation
    (MAC address collisions are still a potential problem)
Receivers find out about sources through out-of-band means (such as a web site)
  Common now anyway

## Slide 13: SSM Advantages (cont’d)
SSM-only implementations are much simpler than the full PIM-SM
  No RP
  No Bootstrap RP Election
  No Register state machine
  No need to keep (*,G), (S,G,rpt) and (*,*,RP) state
  No (*,G) Assert State

## Slide 14: SSM Advantages (cont’d)
Receiver issues a (S,G) join directly
Because the join is to a specific Source IP address, unintended Sources cannot join the transmissions
This is important to broadcasters who want to control their transmissions

## Slide 15: SSM Deployment
If you have PIM-SM deployed, then you can run SSM on the interior of your network
  Just filter out (*,G) joins/leaves on 232 / 8
IGMP v.3 versions are available / coming
  Microsoft “Whistler”
  Linux kernel support available
  Cisco has available stand-alone “v3-lite”
Applications are coming...

## Slide 16: SSM Disadvantages
Requires I GMP v.3, which is not widely deployed
  <draft-ietf-idmr-igmp-v3-05.ps>
  Both applications and edge-routers must be upgraded
(S,G) joins can be issued in the absence of source transmissions, enabling DOS attacks against a source S or its first hop router.

## Slide 17: Multicast and Denial of Service attacks
Multicasting is subject to a number of Denial of Service Attacks.
These can take three basic forms.
  IGMP join messages can be sent to the first hop router for a given (*,G) or (with IGMP v.3) includes for a given (S,G).
  A Host can start issuing multicast data for a particular Group, G, thereby generating (S,G) state
  It is possible in principle to spoof intra-router control packets; however, RPF and other checks make this difficult

## Slide 18: The “RAMEN” Worm as a Multicast DOS
First detected through its effect on the routers
Caused by 40,000+ SA’s being sent in ~ one minute
Short term fix is to rate limit on SA’s or on the port used by the Worm

## Slide 19: Evidence for the MSDP “RAMEN” WORM
From http://www.caida.org/tools/measurement/Mantra/session-mon/session-mon.html

## Slide 20: The Worm exposed
The Ramen WORM at work :
  It scanned a /16 in the Class D space.
  It thus sent one packet to each of ~ 64,000 groups (Class D addresses).
  The FHR encapsulated these and sent them to the RP.
  The RP encapsulated each packet into a Session Announcement and sent these to neighboring RP’s.
  These were then flooded throughout the Internet.
  All of this happened within a few minutes.
  Caused a number of router “melt-downs”
The astounding thing is that this almost certainly was NOT directly aimed at a multicasting DOS.
  Sloppy programming on the port scans!

## Slide 21: Multicast DOS : Rate Limits
Will need a defense in depth against DOS attacks
Rate limits are be needed to limit the spread of these attacks
  IGMP router
    rate limit number of joins and leaves from a host
  PIM routers
    limit groups created by a given source, S.
    rate limit incoming joins and leaves
    rate limit RP register messages at the RP
    rate limit incoming Session Announcements
    rate limit incoming Register messages

## Slide 22: Multicast DOS : ISM vs SSM
Note : FHR = first hop router

## Slide 23: Conclusions
Multicasting will be necessary for truly affordable broadcasts to mass audiences on the Internet.
Adoption of SSM and IGMP v.3 is coming
Need to seriously address DOS sensitivites.
E-mail me at tme@on-the-i.com
FOR MORE INFO...