## Slide 1: ISP Security - Real World Techniques
Version 1.0
Notes: "The Internet is a battleground with the ISP's and their customer right in the middle of the line of fire. What ISPs need to protect themselves are tools and techniques that work in the line of fire. This tutorial will walk ISPs through the five stages of working an attack - preparation, identification, classification, traceback, and reaction. Focus will be placed on techniques that work - with specific vendor features left for other sessions. All the techniques have been validated and proven to be operationally deployable and workable under a condition of network stress. The key objective is to empower other ISPs to deploy these vendor independent technique that will provide a foundation for inter-NOC cooperation to traceback the attacks to their source.“
+ Be Prepared - Section that covers steps ISPs need to do to prepare for ISP Security concerns. Everything from basics on configuration on equipment to testing tools that would be used to identify, classify, traceback, and reack to attacks.
+ DOS/DDOS Identification - Reality Update. What ISPs can do today. This would be a lot with SNMP tracking. Things like watching the difference on the total CPU load vs the interrupt level CPU load that can clue you into either a major CEF problem or a DOS/DDOS.
+ DOS/DDOS Classification. Again, what ISPs can do today. Start from the classic output ACL (all permits) to redirecting flow to the target to a sink hole router to Netflow based classification (for the people who use Netflow). The config example here need to be Cisco and Juniper.
+ DOS/DDOS Traceback. We can start with the classic hop-by-hop ACLs and show why this is not a "operationally feasible" option. Then break into two paths - flow based and backscatter. The objective here would be to get people to do one of them. Backscatter is the easiest to integrate into an operations - plus the same "sink hole" infrastructure can be used for identification and classification phases.
+ DOS/DDOS Reaction. What is can an ISP do? This is where we can get into inter-NOC cooperation. Rate-limiting/ACLs/uRPF are all the easy part. Getting the ISP upstream from the attack to do something is the hard part.

## Slide 2
Brian W Gemberling brian@uu.net
Christopher L. Morrow chris@UU.NET
Barry R. Greene bgreene@cisco.com

## Slide 3: Objective
Empower ISPs to deploy vendor independent security incident techniques that will provide a foundation for inter-NOC cooperation to traceback the attacks to their source.

## Slide 4: Take Note
There are no magic knobs, grand security solutions, or super vendor features that will solve the ISP Security problem.
Likewise, there is no rocket science involved. Just hard work that is within all ISP’s grasp.
What follows are tools and techniques that might or might not work for you.

## Slide 5: Agenda
Six Phases of how a ISP Works a Security Incident
Foundation Techniques
Digression on the Six Phases
URLs

## Slide 6: Six Phases of How and ISP Responds to a Security Incident

## Slide 7: ISP Security Response
ISP’s Operations Team response to a security incident can typically be broken down into six phases:
  Preparation
  Identification
  Classification
  Traceback
  Reaction
  Post Mortem
Notes: <number>
<footer>
<header>
<date/time>

## Slide 8: ISP Security Response
Preparation: All the work the ISP does to prepare he network, create the tools, test the tools, develop the procedures, train the team, and practice.
  Perhaps the most important phase of how a ISP responds to a security incident.
Identification – How do you know you or your customer is under attack?

## Slide 9: ISP Security Response
Classification – Understanding the type of attack and what damage is it causing.
Traceback – From where is the attack originating?
Reaction – Doing something to counter the attack – even if you choose to do nothing.
Post Mortem – Analyzing what just happened. What can be done to build resistance to the attack happening again.

## Slide 10: Foundation Techniques

## Slide 11: Foundation Techniques
Classification and Traceback ACLs
Black Hole Filtering
Sink Hole/Black Hole Route Server
Backscatter Traceback Technique

## Slide 12: Classification and Traceback ACLs
Most common technique used to tweak a router into a pseudo packet sniffer.
  An Access List (ACL) with a series of permit statements are used to view into the traffic flow.
  Access List Entry (ACE) counters are used to find which protocol types are potential culprits.
  Once the protocol type is suspected, another permit ACL with log statements is used to capture some of the packet characteristics.

## Slide 13: Classification and Traceback ACLs
Use ACL to find out the characteristics of the attack
  access-list 169 permit icmp any any echo
  access-list 169 permit icmp any any echo-reply
  access-list 169 permit udp any any eq echo
  access-list 169 permit udp any eq echo any
  access-list 169 permit tcp any any established
  access-list 169 permit tcp any any range 0 65535
  access-list 169 permit ip any any
  interface serial 0
  ip access-group 169 out
Notes: <number>
<footer>
<header>
<date/time>

## Slide 14: Classification and Traceback ACLs
Use the show access-list 169 to see which protocol is the source of the attack:
  Extended IP access list 169
  permit icmp any any echo (2 matches)
  permit icmp any any echo-reply (21374 matches)
  permit udp any any eq echo
  permit udp any eq echo any
  permit tcp any any established (150 matches)
  permit tcp any any (15 matches)
  permit ip any any (45 matches)
Notes: <number>
<footer>
<header>
<date/time>

## Slide 15: Classification and Traceback ACLs
Classification ACLs are applied as close to the customer as possible.
  Mainly on the customer’s ingress interface to the ISP with an output ACL.
Traceback ACLs are usually applied hop by hop – finding the ingress interface of the flow and working up to the next hop.

## Slide 16: Classification and Traceback ACLs
Traceback spoofed source IP addresses using ACLs are a challenge.
Tracing needs to happen hop by hop
The first step is to use the ACL “log-input” function to grab a few packets
Quick in and out is needed to keep the router for overloading with logging interrupts to the CPU
Notes: <number>
<footer>
<header>
<date/time>

## Slide 17: Classification and Traceback ACLs
Preparation
  Make sure your logging buffer on the router is large
  Create the ACL
  Turn off any notices/logging messages to the console or vty (so you can type the command no access-group 170
Notes: <number>
<footer>
<header>
<date/time>

## Slide 18: Classification and Traceback ACLs
  access-list 170 permit icmp any any echo
  access-list 170 permit icmp any any echo-reply log-input
  access-list 170 permit udp any any eq echo
  access-list 170 permit udp any eq echo any
  access-list 170 permit tcp any any established
  access-list 170 permit tcp any any
  access-list 170 permit ip any any
  interface serial 0
  ip access-group 170 out
  ! Wait a short time - (i.e 10 seconds)
  no ip access-group 170 out
Notes: <number>
<footer>
<header>
<date/time>

## Slide 19: Classification and Traceback ACLs
Validate the capture with show access-list 170; make sure it the packets we counted
Check the log with show logging for addresses:
  %SEC-6-IPACCESSLOGDP: list 170 permit icmp 192.168.212.72 (Serial0 *HDLC*) -> 198.133.219.25 (0/0), 1 packet
  %SEC-6-IPACCESSLOGDP: list 170 permit icmp 172.16.132.154 (Serial0 *HDLC*) -> 198.133.219.25 (0/0), 1 packet
  %SEC-6-IPACCESSLOGDP: list 170 permit icmp 192.168.45.15 (Serial0 *HDLC*) -> 198.133.219.25 (0/0), 1 packet
  %SEC-6-IPACCESSLOGDP: list 170 permit icmp 192.168.45.142 (Serial0 *HDLC*) -> 198.133.219.25 (0/0), 1 packet
  %SEC-6-IPACCESSLOGDP: list 170 permit icmp 172.16.132.47 (Serial0 *HDLC*) -> 198.133.219.25 (0/0), 1 packet
Notes: <number>
<footer>
<header>
<date/time>

## Slide 20: Traceback via Hop by Hop Technique
Hop by hop tracebacks takes time
  Starts from the beginning and traces to the source of the problem
  Needs to be done on each router
  Often requires splitting—tracing two separate paths
  Speed is the limitation of the technique
Inside
Outside
Target
Source
Notes: <number>
<footer>
<header>
<date/time>

## Slide 21: Traceback via Hop by Hop Technique
Peer B
Peer A
IXP-W
IXP-E
Upstream A
Upstream A
Upstream B
Upstream B
POP
Target
X
Hop by Hop Goes from Router to Router
Notes: <number>
<footer>
<header>
<date/time>

## Slide 22: Classification and Traceback ACLs
See the following URLs for vendor details:
  http://www.cisco.com/warp/public/707/22.html
  http://www.juniper.net/techcenter/app_note/350001.html

## Slide 23: Foundation Techniques
Classification and Traceback ACLs
Black Hole Filtering
Sink Hole/Black Hole Route Server
Backscatter Traceback Technique

## Slide 24: Black Hole Filtering
Black Hole Filtering or Black Hole Routing forwards a packet to a router’s bit bucket.
  Also known as “route to Null0”
Works only on destination addresses, since it is really part of the forwarding logic.
Forwarding ASICs are designed to work with routes to Null0 – dropping the packet with minimal to no performance impact (depending on the forwarding ASIC).
Used for years as a means to “black hole” un wanted packets.

## Slide 25: Black Hole Filtering
FIB
---------------------
---------------------
---------------------
---------------------
---------------------
---------------------
---------------------
---------------------
Ingress ACL
---------------------
---------------------
---------------------
---------------------
Null0
Packets Arrive
Route to the Bit Bucket
Saves on CPU and ACL processing

## Slide 26: Remotely Triggered Black Hole Filtering
A simple static route and BGP will allow an ISP to trigger network wide black holes as fast as iBGP can update the network.
This provides ISPs a tool that can be used to respond to security related events or used for DOS/DDOS Backscatter Tracebacks.

## Slide 27: Remotely Triggered Black Hole Filtering - Preparation
  Select a small block that will not be used for anything other than black hole filtering. Test Net (192.0.2.0/24) is optimal since it should not be on the Net and is not really used.
  Put a static route with Test Net – 192.0.2.0/24 to Null 0 on every router on the network.
  Prepare a BGP speaking router that will be used to announce the network to be Black Holed (see config example on next slide).

## Slide 28: Remotely Triggered Black Hole Filtering - Preparation
router bgp 109
.
redistribute static route-map static-to-bgp
.
!
route-map static-to-bgp permit 10
match tag 66
set ip next-hop 192.0.2.1
set local-preference 50
set community no-export
set origin igp
!
Route-map static-to-bgp permit 20

## Slide 29: Remotely Triggered Black Hole Filtering - Activation
  ISP adds a static route of the destination address they wish to black hole to the advertising router. The static is added with the “tag 66” to keep it separate from other statics on the router.
    ip route 171.68.1.1 255.255.255.255 Null0 Tag 66
  BGP Advertisement goes out to all BGP speaking routers.
  Router hear the announcement, glues it to the existing static on the route, and changes the next-hop for the BGP advertised route to Null0 – triggering black hole routing.

## Slide 30: Remotely Triggered Black Hole Filtering - Activation
BGP Best Path Selection
BGP 109’s RIB
AS 65000’s
Routes
AS 109’s Routes
AS 300’s Routes
OSPF RIB
Static and Connected Routes
FIB
FIB Best Path Selection
(Unless Multi-Path)
FIB Glues 171.68.1.1’s next-hop to Null0 triggering the black hole filtering
192.0.2.0/24 = Null0
192.0.2.0/24 = Null0
171.68.1.1 next-hop = 192.0.2.1 w/ no-export
171.68.1.1 next-hop = 192.0.2.1
Notes: <number>
<footer>
<header>
<date/time>

## Slide 31: Remotely Triggered Black Hole Filtering - Activation
BGP Sent – 171.68.1.0/24 Next-Hop = 192.0.2.1
Static Route in Edge Router – 192.0.2.1 = Null0
171.68.1.0/24 = 192.0.2.1 = Null0
Next hop of 171.68.1.0/24 is now equal to Null0
Notes: <number>
<footer>
<header>
<date/time>

## Slide 32: Remotely Triggered Black Hole Filtering - Activation
NOC
A
B
C
D
E
F
G
iBGP Advertises List of Black Holed Prefixes
Target
Peer B
Peer A
IXP-W
IXP-E
Upstream A
Upstream B
Upstream B
POP
Upstream A
Notes: <number>
<footer>
<header>
<date/time>

## Slide 33: Gotchas with Black Hole Filtering
Routers were designed to forward traffic, not drop traffic.
ASIC Based Forwarding can drop traffic at line rate.
Processor Based Forwarding can have problems dropping large amounts of data.
Remember the old shunt technique ….

## Slide 34: Gotchas with Black Hole Filtering
Back in the days when this was in the core of the Internet …..
All “drops” to Null0 were process switched.
Fast Drops fixed the problem for a while, but traffic loads increased to the to where they could not drop at line rate anymore.
Bottomline – Software based forwarding routers (any vendor) can forward faster then they can drop.

## Slide 35: Black Hole Shunt
Black Hole Shunts are used to forward traffic out a spoofed interface.
  Classic Example: AUI/BNC Transceiver with a T connector. A static MAC address is used with a static route.
AUI to
BNC
Packet Flow
Router
Static Route to Spoofed Ethernet

## Slide 36: Black Hole Shunt
Some ISPs used Black Hole Shunts during Code Red.
  Routers that injected Default Sucked all traffic to them.
Packet Flow
Router
Static Route to Spoofed POS Interface

## Slide 37: Foundation Techniques
Classification and Traceback ACLs
Black Hole Filtering
Sink Hole/Black Hole Route Server
Backscatter Traceback Technique

## Slide 38: Sink Hole Routers/Networks
Sink Holes are a the network equivalent of a honey pot.
  BGP speaking Router or Workstation that built to suck in attacks.
  Used to redirect attacks away from the customer – working the attack on a router built to withstand the attack.
  Used to monitor attack noise, scans, and other activity (via the advertisement of default)

## Slide 39: Sink Hole Routers/Networks
Target of Attack
172.168.20.1 is attacked
172.168.20.0/24 – target’s network
Sink Hole Network

## Slide 40: Sink Hole Routers/Networks
Target of Attack
172.168.20.1 is attacked
172.168.20.0/24 – target’s network
Router advertises 172.168.20.1/32
Sink Hole Network

## Slide 41: Sink Hole Routers/Networks
Attack is pulled off customer and your aggregation router.
Can now do classification ACLs, Flow Analysis, Sniffer Capture, Traceback, etc.
Objective is to minimize the risk to the network while working the attack incident.
Target of Attack
172.168.20.1 is attacked
172.168.20.0/24 – target’s network
Router advertises 172.168.20.1/32
Sink Hole Network

## Slide 42: Sink Hole Routers/Networks
Advertising Default from the Sink Hole will pull down all sort of junk traffic.
  Customer Traffic when circuits flap.
  Network Scans
  Failed Attacks
  Code Red/NIMDA
  Backscatter
Can place tracking tools and IDA in the Sink Hole network to monitor the noise.
Customers
172.168.20.1 is attacked
172.168.20.0/24 – target’s network
Router Advertises Default
Sink Hole Network

## Slide 43: Foundation Techniques
Classification and Traceback ACLs
Black Hole Filtering
Sink Hole/Black Hole Route Server
Backscatter Traceback Technique

## Slide 44: Backscatter Traceback Technique
Created by Chris Morrow and Brian Gemberling @ UUNET as a means of finding the entry point of a spoofed DOS/DDOS.
  http://www.secsup.org/Tracking/
Combines the Sink Hole router, Backscatter Effects of Spoofed DOS/DDOS attacks, and remote triggered Black Hole Filtering to create a traceback system that provides a result within 10 minutes.

## Slide 45: Backscatter Traceback Technique
What is backscatter?
FIB
---------------------
---------------------
192.168.1.0 = Null0
---------------------
---------------------
---------------------
---------------------
---------------------
ICMP Process
---------------------
---------------------
---------------------
---------------------
Null0
Packets Arrive SRC = 171.68.10.70
DST = 192.168.1.1
Packets whose destination is unreachable (even Null0) will have a ICMP Unreachable sent back. This “unreachable noise” is backscatter.
ICMP Unreachable to SRC 171.68.10.70

## Slide 46: Backscatter Traceback Preparation
  Sink Hole Router/Network connected to the network and ready to classify the traffic. Like before, BGP Route Reflector Client, device to analyze logs, etc.
    Can use one router to do both the route advertisement and logging OR break them into two separation routers – one for route advertisement and the other to accept/log traffic
    Can be used for other Sink Hole functions while not using the traceback technique.
    Sink Hole Router can be a iBGP Route Reflector into the network.

## Slide 47: Backscatter Traceback Preparation
Peer B
Peer A
IXP-W
IXP-E
Upstream A
Upstream A
Upstream B
Upstream B
POP
Target
X
NOC
G
Sink Hole Network
Sink Hole Router Ready to advertise routes and accept traffic.
171.68.19.0/24
171.68.19.1
Notes: <number>
<footer>
<header>
<date/time>

## Slide 48: Backscatter Traceback Activation
!
router bgp 31337
!
! set the static redistribution to include a route-map so we can filter
! the routes somewhat... or at least manipulate them
! redistribute static route-map static-to-bgp
!
! add a stanza to the route-map to set our special next hop
!
route-map static-to-bgp permit 5
match tag 666
set ip next-hop 172.20.20.1
set local-preference 50
set origin igp

## Slide 49: Backscatter Traceback Activation
# Setup the bgp protocol to export our special policy, like redistributing, NOTE: "XXX" # is the IBGP bgp group... we don't want to send this to customers do we?
#
set protocols bgp group XXX export BlackHoleRoutes
#
# Now, setup the policy option for BlackHoleRoutes, like a route-map if static route
# with right tag, set local-pref low, internal, no-export can't leak these or Tony Bates
# will have a fit, and set the nexthop to the magical next-hop.
#
set policy-statement BlackHoleRoutes term match-tag666 from protocol static tag 666
set policy-statement BlackHoleRoutes term match-tag666 then local-preference 50
set policy-statement BlackHoleRoutes term match-tag666 then origin igp
set policy-statement BlackHoleRoutes term match-tag666 then community add no-export
set policy-statement BlackHoleRoutes term match-tag666 then nexthop 172.20.20.1
set policy-statement BlackHoleRoutes term match-tag666 then accept

## Slide 50: Backscatter Traceback Preparation
  All edge devices (routers, NAS, IXP Routers, etc) with a static route to Null0. The Test-Net is a safe address to use (192.0.2.0/24) since no one is using it.
    Cisco: ip route 172.20.20.1 255.255.255.255 Null0
    Juniper: set routing-options static route 172.20.20.1/32 reject install
    Routers also need to have ICMP Unreachables working. If you have ICMP Unreachables turned off (i.e. no ip unreachables on a Cisco), then make sure they are on.
    If ICMP Unreachable Overloads are a concern, use a ICMP Unreachable Rate Limit (i.e. ip icmp rate-limit unreachable command on a Cisco).

## Slide 51: Backscatter Traceback Preparation
Peer B
Peer A
IXP-W
IXP-E
Upstream A
Upstream A
Upstream B
Upstream B
POP
Target
X
NOC
G
Sink Hole Network
171.68.19.0/24
171.68.19.1
Edge Router with Test-Net to Null0
Edge Router with Test-Net to Null0
Edge Router with Test-Net to Null0
Notes: <number>
<footer>
<header>
<date/time>

## Slide 52: Backscatter Traceback Preparation
  Sink Hole Router advertising a large block of un-allocated address space with the BGP no-export community and BGP Egress route filters to keep the block inside. 96.0.0.0/3 is an example.
    Check with IANA for unallocated blocks: www.iana.org/assignments/ipv4-address-space
    BGP Egress filter should keep this advertisement inside your network.
    Use BGP no-export community to insure it stays inside your network.

## Slide 53: Backscatter Traceback Preparation
Peer B
Peer A
IXP-W
IXP-E
Upstream A
Upstream A
Upstream B
Upstream B
POP
Target
X
NOC
G
Sink Hole Network
Sink Hole Router advertising 96.0.0.0/3
171.68.19.0/24
171.68.19.1
Notes: <number>
<footer>
<header>
<date/time>

## Slide 54: Backscatter Traceback Activation
Activation happens when an attack has been identified.
Basic Classification should be done to see if the backscatter traceback will work:
  May need to adjust the advertised block.
  Statistically, most attacks have been spoofed using the entire Internet block.

## Slide 55: Backscatter Traceback Activation
  Sink Hole Router Advertises the /32 under attack into iBGP with.
    Advertised with a static route with the “666” tag:
    ip route victimip 255.255.255.255 Null0 tag 666
    or
    set routing-options static route victimip/32 discard tag 666
    The static triggers the routers to advertise the customer’s prefix

## Slide 56: Backscatter Traceback Activation
Peer B
Peer A
IXP-W
IXP-E
Upstream A
Upstream A
Upstream B
Upstream B
POP
Target
X
NOC
G
Sink Hole Network
Sink Hole router advertises the /32 under attack with next-hop equal to the Test-Net
171.68.19.0/24
171.68.19.1
Edge Routers start dropping packets to the/32
Edge Routers start dropping packets to the/32
Notes: <number>
<footer>
<header>
<date/time>

## Slide 57: Backscatter Traceback Activation
  Black Hole Filtering is triggered by BGP through out the network. Packets to the target get dropped. ICMP Unreachable Backscatter starts heading for 96.0.0.0/3.
    Access list is used on the router to find which routers are dropping packets.
    access-list 101 permit icmp any any unreachables log access-list 101 permit ip any any

## Slide 58: Backscatter Traceback Activation
Peer B
Peer A
IXP-W
IXP-E
Upstream A
Upstream A
Upstream B
Upstream B
POP
Target
X
NOC
G
Sink Hole Network
Sink Hole Router receive the backscatter to 96/3 with entry points of the attack
171.68.19.0/24
171.68.19.1
ICMP Unreachable backscatter will start sending packets to 96/3
ICMP Unreachable backscatter will start sending packets to 96/3
Notes: <number>
<footer>
<header>
<date/time>

## Slide 59: Backscatter Traceback Activation
SLOT 5:3w1d: %SEC-6-IPACCESSLOGDP: list 150 permitted icmp 171.68.66.18
-> 96.47.251.104 (3/1), 1 packet
SLOT 5:3w1d: %SEC-6-IPACCESSLOGDP: list 150 permitted icmp 171.68.66.18
-> 96.70.92.28 (3/1), 1 packet
SLOT 5:3w1d: %SEC-6-IPACCESSLOGDP: list 150 permitted icmp 171.68.66.18
-> 96.222.127.7 (3/1), 1 packet
SLOT 5:3w1d: %SEC-6-IPACCESSLOGDP: list 150 permitted icmp 171.68.66.18
-> 96.96.223.54 (3/1), 1 packet
SLOT 5:3w1d: %SEC-6-IPACCESSLOGDP: list 150 permitted icmp 171.68.66.18
-> 96.14.21.8 (3/1), 1 packet
SLOT 5:3w1d: %SEC-6-IPACCESSLOGDP: list 150 permitted icmp 171.68.66.18
-> 96.105.33.126 (3/1), 1 packet
SLOT 5:3w1d: %SEC-6-IPACCESSLOGDP: list 150 permitted icmp 171.68.66.18
-> 96.77.198.85 (3/1), 1 packet
SLOT 5:3w1d: %SEC-6-IPACCESSLOGDP: list 150 permitted icmp 171.68.66.18
-> 96.50.106.45 (3/1), 1 packet

## Slide 60: ISP Security Response
ISP’s Operations Team response to a security incident can typically be broken down into six phases:
  Preparation
  Identification
  Classification
  Traceback
  Reaction
  Post Mortem
Notes: <number>
<footer>
<header>
<date/time>

## Slide 61: Be Prepared

## Slide 62: Preparation
Preparation is critical!
  You know your customers are going to be attacked
  It is not a matter of if but how often and how hard
  The Internet is not a nice place anymore!
  Think battle plans
Militaries know the value of planning, practice, drilling and simulation
  Those that are prepared will be victorious.
Notes: <number>
<footer>
<header>
<date/time>

## Slide 63: What Do ISPs Need to Do?
2) Secure Resources
Firewall, Encryption, Authentication, Audit
1) ISP’s Security Policy
3) Monitor and Respond
Intrusion Detection, work the incidence,
4) Test, Practice, Drill
Vulnerability Scanning
5) Manage and Improve
Post Mortem, Analyze the Incident, modify the plan/procedures
Security incidence are a normal part of an ISP’s operations!
Notes: <number>
<footer>
<header>
<date/time>

## Slide 64: Preparation
?
The problem - Most ISP NOCs:
  Do not have security plans
  Do not have security procedures
  Do not train in the tools or procedures
  OJT (on the job training)—learn as it happens
Notes: <number>
<footer>
<header>
<date/time>

## Slide 65: Preparation
It is imperative that an ISP’s operations team prepare.
  Contacts for all ISPs who you inter-connect (peers, customers, and upstreams)
  Document your policies. Will you help your customers? Will you classify the attacks? Will you traceback the attacks? Will you drop the attacks on your infrastructure?

## Slide 66: Preparation
Prepare you Tools!
  Do you have your ACLs created?
  Do you have your scripts created?
  Have you built and tested your Sink Hole and Backscatter tools?

## Slide 67: Preparation
Test you Tools before you really need to use them!
  Have you tried putting a classification ACL on various parts of your network?
  Have you tested your scripts to insure they will work?
  Have you simulated attacks?

## Slide 68: Preparation
Red Team/Blue Team exercises
  Divide up into two teams — one defends, one attacks
  Referee assigns the attackers with an objective (get this file, deface the web site, take down the target, etc.)
  Defenders use network/system designs and tools/procedures to defend the target
  One of the most effective ways to get your staff into the depths of TCP/IP, OS, applications, and security
Notes: <number>
<footer>
<header>
<date/time>

## Slide 69: Preparation
Audit your network configs.
  Secure the Router/Switch
  Secure the Routing Protocol
  Secure the Network

## Slide 70: Preparation
Know your Equipment and Infrastructure:
  Know the Performance Envelop of all your equipment (routers, switches, workstation, etc). You need to know what your equipment is really capable of doing. If you cannot do it your self, make is a purchasing requirement.
  Know the capabilities of your network. If possible, test it. Surprises are not kind during a security incident.

## Slide 71: What Do ISPs Need to Do?
2) Secure Resources
Firewall, Encryption, Authentication, Audit
1) ISP’s Security Policy
3) Monitor and Respond
Intrusion Detection, work the incidence,
4) Test, Practice, Drill
Vulnerability Scanning
5) Manage and Improve
Post Mortem, Analyze the Incident, modify the plan/procedures
Security incidence are a normal part of an ISP’s operations!
Notes: <number>
<footer>
<header>
<date/time>

## Slide 72: DOS/DDOS Identification

## Slide 73: Identifying an Attack
When are we being probed?
  Probes happen all the time; which ones are important?
  Probes precede an attack; if you can track specific probes, you might get a heads up that an attack is imminent
Notes: <number>
<footer>
<header>
<date/time>

## Slide 74: Identifying an Attack
When are we your customers being attacked?
  #1 way to identify that there is an attack in progress is when a customer calls the NOC
  New ISP oriented IDS tool are in the works

## Slide 75: Identifying an Attack
When are you being attack?
  NOC Alerts – is a problem in the network, a surge in traffic, a killer app, or someone attacking your network?

## Slide 76: Identifying an Attack
SNMP Data abortion can signal a network problem or a security incident.
CPU spike when nothing else is happening on the network and with no one working on the router.

## Slide 77: Identifying an Attack
What about those Intrusion Detection Systems (IDS)?
  Try them.
  Sink Hole Network is a good place to put them (sucks in all the junk and lets the IDS sort it out).
  Always be on the lookout for a new tool, trick, feature, or capability.

## Slide 78: DOS/DDOS Classification

## Slide 79: Classifying an Attack
How are we being attacked?
  Once the attack starts, how do you find specifics of the attack?
  Customer might provide information
  Tools and procedures needed inside an ISP to specific information on the attack
  Minimum source addresses and protocol type
Notes: <number>
<footer>
<header>
<date/time>

## Slide 80: Classifying an Attack
Classification is critical to your reaction. If you are not sure of the characteristics of the attack, your reaction to the attack could add to the problem.

## Slide 81: Classifying an Attack
Use ACL with permit for a group of protocols to drill down to the protocol
  Extended IP access list 169
  permit icmp any any echo (2 matches)
  permit icmp any any echo-reply (21374 matches)
  permit udp any any eq echo
  permit udp any eq echo any
  permit tcp any any established (150 matches)
  permit tcp any any (15 matches)
  permit ip any any (45 matches)
  See http://www.cisco.com/warp/public/707/22.html
Notes: <number>
<footer>
<header>
<date/time>

## Slide 82: Sink Hole Classification Technique
Is it worth the risk to make config changes while a customer is under attack on a aggregation router with hundreds of customers connected to it?
  Config changes when the network is under duress can and will cause more problems (it is not an “IOS” think – this applies to any network)
What would help is if the attack flow can be shifted from the target (i.e. customer) to some other router where the risk is manageable.
Enter the Sink Hole Router.
  Similar to a Unix Honey Pot.

## Slide 83: Sink Hole Classification Technique
Sink Hole Router Preparation:
  Router with really fast packet dropping capability, software features, and a connection to the network (were traffic to it would not endanger the network). Think 7200 with the fastest NPE you can get.
  BGP session (Route Reflector Client). The target’s more specific address will get advertised from here.
  Packet Filters, syslog exports, and a way to analyze the logs from the ACL’s log-input.

## Slide 84: Sink Hole Classification Technique
Peer B
Peer A
IXP-W
IXP-E
Upstream A
Upstream A
Upstream B
Upstream B
POP
Target
X
NOC
G
Sink Hole Network
Sink Hole Router Ready to advertise a Target’s more specific address
171.68.19.0/24
171.68.19.1
Notes: <number>
<footer>
<header>
<date/time>

## Slide 85: Sink Hole Classification Technique
Sink Hole Classification – Activation
  Customer notifies ISP that they are under attack and need help. ISP lets the customer know that they will take the targeted host’s IP address and redirect it to classify and traceback (see Backscatter Traceback technique).
  Sink Hole Router advertises the /32 address that is under attack.
  All traffic for that /32 shifts to the Sink Hole Router. ACL Packet Classification, Netflow Classification, or host based (specialized box) is done on a section of the ISPs network built to be attacked.
  Massive Aggregation Router is not touched.

## Slide 86: Sink Hole Classification Technique
Peer B
Peer A
IXP-W
IXP-E
Upstream A
Upstream A
Upstream B
Upstream B
POP
Target
NOC
G
Sink Hole Network
Sink Hole Router advertises 171.68.19.1/32
171.68.19.0/24
171.68.19.1
171.68.19.1
X
Host Not Reachable while Classification and Traceback in progress.
Notes: <number>
<footer>
<header>
<date/time>

## Slide 87: DOS/DDOS Traceback

## Slide 88: Traceback the Attack
From where are we being attacked (inside or outside)?
  Once you have a fundamental understanding of the type of attack (source address and protocol type), you then need to track back to the ingress point of the network
  Three techniques— hop by hop, jump to ingress, and backscatter.
Notes: <number>
<footer>
<header>
<date/time>

## Slide 89: Traceback via Hop by Hop Technique
Hop by hop tracebacks takes time
  Starts from the beginning and traces to the source of the problem
  Needs to be done on each router
  Often requires splitting—tracing two separate paths
  Speed is the limitation of the technique
Inside
Outside
Target
Source
Notes: <number>
<footer>
<header>
<date/time>

## Slide 90: Traceback via Hop by Hop Technique
Peer B
Peer A
IXP-W
IXP-E
Upstream A
Upstream A
Upstream B
Upstream B
POP
Target
X
Hop by Hop Goes from Router to Router
Notes: <number>
<footer>
<header>
<date/time>

## Slide 91: Traceback via the Jump to Ingress Technique
Jump to ingress tracebacks divides the problem in half
  Is the attack originating from inside the ISP or outside the ISP?
  Jumps to the ISP’s ingress border routers to see if the attack is entering the network from the outside
  Advantage of speed—are we the source or someone else the source?
Inside
Outside
Target
Source
Notes: <number>
<footer>
<header>
<date/time>

## Slide 92: Traceback via the Jump to Ingress Technique
Target
X
Jump to Ingress Uses Netflow on the Ingress Routers to Spot the Attack
Peer B
Peer A
IXP-W
IXP-E
Upstream A
Upstream A
Upstream B
Upstream B
POP
Notes: <number>
<footer>
<header>
<date/time>

## Slide 93: Traceback the Attack
Two techniques for hop by hop or jump to ingress.
  Apply temporary ACLs with log-input and examine the logs (like step 2)
  Query Netflow’s flow table (if show ip cache-flow is turned on)
Notes: <number>
<footer>
<header>
<date/time>

## Slide 94: Traceback with ACLs
  access-list 170 permit icmp any any echo
  access-list 170 permit icmp any any echo-reply log-input
  access-list 170 permit udp any any eq echo
  access-list 170 permit udp any eq echo any
  access-list 170 permit tcp any any established
  access-list 170 permit tcp any any
  access-list 170 permit ip any any
  interface serial 0
  ip access-group 170 out
  ! Wait a short time - (i.e 10 seconds)
  no ip access-group 170 out
Notes: <number>
<footer>
<header>
<date/time>

## Slide 95: Traceback with ACLs
Original technique for doing tracebacks
Hazard—inserting change into a network that is under attack
Hazard—log-input requires the forwarding ASIC to punt the packet to capture log information
BCP is to apply the filter, capture just enough information, then remove the filter
Notes: <number>
<footer>
<header>
<date/time>

## Slide 96: Traceback with Netflow
Beta-7200-2>sh ip cache 198.133.219.0 255.255.255.0 verbose flow
IP packet size distribution (17093 total packets):
1-32 64 96 128 160 192 224 256 288 320 352 384 416 448 480
.000 .735 .088 .054 .000 .000 .008 .046 .054 .000 .009 .000 .000 .000 .000
512 544 576 1024 1536 2048 2560 3072 3584 4096 4608
.000 .000 .000 .000 .000 .000 .000 .000 .000 .000 .000
IP Flow Switching Cache, 1257536 bytes
3 active, 15549 inactive, 12992 added
210043 ager polls, 0 flow alloc failures
last clearing of statistics never
Protocol Total Flows Packets Bytes Packets Active(Sec) Idle(Sec)
-------- Flows /Sec /Flow /Pkt /Sec /Flow /Flow
TCP-Telnet 35 0.0 80 41 0.0 14.5 12.7
UDP-DNS 20 0.0 1 67 0.0 0.0 15.3
UDP-NTP 1223 0.0 1 76 0.0 0.0 15.5
UDP-other 11709 0.0 1 87 0.0 0.1 15.5
ICMP 2 0.0 1 56 0.0 0.0 15.2
Total: 12989 0.0 1 78 0.0 0.1 15.4
SrcIf SrcIPaddress DstIf DstIPaddress Pr SrcP DstP Pkts
Fa1/1 192.168.45.142 POS1/0 198.133.219.25 11 008A 008A 1
Fa1/1 192.168.45.113 POS1/0 198.133.219.25 11 0208 0208 1
Fa1/1 172.16.132.154 POS1/0 198.133.219.25 06 701D 0017 63
Spoofed Flows are Tracks in Netflow!
Notes: <number>
<footer>
<header>
<date/time>

## Slide 97: Traceback with Netflow
Generic ways to use the Netflow command:
  show ip cache <addr> <mask> verbose flow
  show ip cache flow | include <addr>
  Proactive approach—create scripts …...
    ssh -x -t -c [des|3des] -l <username> <IPAddr> “show ip cache <addr> <mask> verbose flow”
Notes: <number>
<footer>
<header>
<date/time>

## Slide 98: Traceback with Netflow
GSR—use the show controllers with sample Netflow (if LC supports SNF)
  GSR-2# exec slot 0 sh ip cache <addr> <mask> verbose flow
7500 with dCEF—CSCdp91364.
  7500# exec slot 0 sh ip cache <addr> <mask> verbose flow
Remember! execute-on all to get Netflow from all the LC/VIPs.
Notes: <number>
<footer>
<header>
<date/time>

## Slide 99: Traceback with Netflow
Key advantage of Netflow:
  No changes to the router while the network is under attack; passive monitoring
  Scripts can be used to poll and sample throughout the network
  IDS products can plug into Netflow
  Working on a MIB for SNMP access
Notes: <number>
<footer>
<header>
<date/time>

## Slide 100: Backscatter Traceback Technique
Three key advantages:
  Reduced Operational Risk to the Network while traceback is in progress.
  Speedy Traceback
  Ability to hand off from one ISP to another – potentially tracing back to it’s source.

## Slide 101: DOS/DDOS Reaction

## Slide 102: DOS/DDOS Reaction
Remember – once you actively do something to mitigate the attack, you have made a choice of entering the game. You now become a fair game target.
It is OK to make a choice to do nothing. You’ve classified and done the traceback for your customer.
It is OK to continue the traceback to the next ISPs upstream of the attack.

## Slide 103: React to the Attack
Doing something to mitigate the impact of the attack OR stop the attack
  Options can be everything from do nothing (doing something might cause other problems) to unplug from the source of the attack (another country during a cyber war attack)
Most ISPs try to help their customers
  Rate-limit the attack
  Drop the packets based on a list of source addresses
Reactions need to be fast and flexible
Notes: <number>
<footer>
<header>
<date/time>

## Slide 104: React to the Attack
Three techniques used to drop or rate limit:
  ACLs—Manual upload
  uRPF—Remote trigger via BGP
  CAR—Manual upload or remote trigger via BGP
Notes: <number>
<footer>
<header>
<date/time>

## Slide 105: Post Mortem

## Slide 106: Post Mortem
Learning from your mistakes is essential.
Do not wait until the next attack to implement the lessons of the last attack.
  Take time after each incident to see if processes, procedures, tools, techniques, and configurations can be improved.
  It is an arms race. Those who learn from this mistakes excel.

## Slide 107: Post Mortem
Fighting the Last War is the #2 mistake of military planner.
Underestimating the capabilities and commitment of your enemy is the #1 mistake of military planners.
This observation directly applies to ISP Security.

## Slide 108: Default Routes, ISPs, and Security

## Slide 109: Avoid Default Routes
ISPs with full BGP feeds should avoid default routes.
DOS/DDOS attack use spoofed addresses from the un-allocated IPV4 space.
  See http://www.iana.org/assignments/ipv4-address-space for the latest macro allocations.
Backscatter traffic from DOS/DDOS targets need to go somewhere. If there is a default, then this traffic will do to this one router and get dropped.
Dropping backscatter traffic might overload the router.

## Slide 110: Network with Default Route – Pointing to Upstream A
Peer B
Peer A
IXP-W
IXP-E
Upstream A
Upstream A
Upstream B
Upstream B
POP
Target
X
NOC
G
Default Route to Upstream A
Backscatter Traffic to 96/6


Notes: <number>
<footer>
<header>
<date/time>

## Slide 111: Network with Default Route – But not Pointing to Upstream
Peer B
Peer A
IXP-W
IXP-E
Upstream A
Upstream A
Upstream B
Upstream B
POP
Target
X
NOC
G
Default Route (but not pointing to upstream)
Backscatter Traffic to 96/6

Notes: <number>
<footer>
<header>
<date/time>

## Slide 112: Network with No Default Route
Peer B
Peer A
IXP-W
IXP-E
Upstream A
Upstream A
Upstream B
Upstream B
POP
Target
X
NOC
G
Backscatter Traffic to 96/6

Notes: <number>
<footer>
<header>
<date/time>

## Slide 113: Default Route and ISP Security - Guidance
Engineer Default Route with ISP Security as one of the factors.
  Most just engineer default with routing/forwarding as the only factor
If you need to use default, best to forward it upstream or to a Sink-Hole network engineered for packet drops.

## Slide 114: DDoS Links
http://www.denialinfo.com/
http://www.staff.washington.edu/dittrich
http://www.fbi.gov/nipc/trinoo.htm
http://www.sans.org/y2k/DDoS.htm
http://www.nanog.org/mtg-9910/robert.html
http://cve.mitre.org/
http://packetstorm.securify.com/distributed/
http://www.cisco.com/public/cons/isp/security/
Notes: <number>
<footer>
<header>
<date/time>